## Slide 1
CASE STUDY
Enabling rpcd on the RDK Stack
Bridging the OpenWrt ubus/rpcd ecosystem into RDK-B (Broadband) and RDK-V (Video) — architecture, integration strategy, and where it breaks down
The short version: rpcd is structurally an OpenWrt component. It has no bus to register on and no config tree to read on RDK — this isn't a recompile problem, it's an architectural integration problem.
RDK Dispatcher Project · Architecture & Integration Review

## Slide 2
01 — MOTIVATION
Why you'd even want this
The tooling-uniformity case, not a platform swap. Operators and ODMs with existing OpenWrt/LuCI tooling — dashboards, automation scripts, monitoring agents — built against ubus's wire protocol and rpcd's object/method/ACL model want that same tooling to work uniformly across a fleet that mixes pure-OpenWrt CPE with RDK-based CPE (gateways and/or STBs).
THE GOAL, PRECISELY
Expose a rpcd-compatible RPC facade on top of RDK's existing internals — not replace RDK's IPC with ubus.
This single framing decision is what makes the rest of the case study tractable — it turns "port rpcd to RDK" into "bridge rpcd into RDK's real buses," which is a fundamentally more achievable ask.
rpcd on RDK — Case Study
2

## Slide 3
02 — THE REAL STACK
What RDK actually uses today
Two profiles, two completely different IPC realities — neither is ubus.
RDK-B — Broadband
RBUS — the primary bus, explicitly replacing D-Bus for performance. Three layers: RBUS API (TR-181-aligned properties/methods/events), RBUS-Core (dispatch, pub/sub, discovery), and rtMessage (binary protocol over Unix socket/TCP). rtrouted brokers every RBUS connection — the same role ubusd plays, completely different wire format. Config/state: TR-181 data model, persisted via PSM + legacy SysCfg — not uci.
RDK-V — Video
IARM-Bus — older, lower-level: platform-agnostic events/RPC between daemons (power state, HDMI hotplug). Thunder (WPEFramework) — layered on since RDK-V 4: plugin-based device abstraction, exposed via COM-RPC (plugin-to-plugin) and JSON-RPC over WebSocket. Auth: a Security Agent plugin issues tokens over COM-RPC, checked against a permissions file.
rpcd on RDK — Case Study
3

## Slide 4
A parallel worth naming up front
Thunder already is, architecturally, an answer to almost the exact problem uhttpd + rpcd solves.
A plugin-loading RPC daemon, reachable over HTTP/JSON-RPC from a browser, with its own token-based session/ACL layer gating which plugin or method a given caller may invoke — the same category of thing this project's own ubus/rpcd container demo already provides for OpenWrt.
That parallel matters directly for the strategy discussion ahead: on RDK-V, adding rpcd mostly duplicates a solved problem. On RDK-B — which has no native browser-facing RPC/token story — it doesn't.
rpcd on RDK — Case Study
4

## Slide 5
03 — THE MISMATCH
The architectural mismatch, side by side
 | ubus / rpcd (OpenWrt) | RDK-B | RDK-V
Bus / broker | ubusd — binary blob_attr over Unix socket | rtrouted (RBUS) — binary rtMessage over Unix socket/TCP | IARM-Bus (low-level) + Thunder's own COM-RPC/JSON-RPC dispatch
Config / data model | uci flat config files (/etc/config/*) | TR-181 data model, backed by PSM + SysCfg | Largely non-uci: RFC + plugin-specific config, no unified TR-181 layer
Plugin loading | dlopen() a .so exporting struct rpc_plugin, or exec a script | Each CCSP/RBUS component is its own long-running daemon process | dlopen()'d .so, but against a C++ base-class/COM-RPC ABI
Session / auth | session.login / session.access, JSON ACL groups | RBUS's own independent ACL configuration | Security Agent + token + permissions file
Browser-facing RPC | uhttpd + uhttpd_ubus.so | No default bridge — would need building | Native: JSON-RPC over WebSocket
Every row is a place where dropping rpcd onto RDK “as-is” has nothing to attach to — no ubusd, no uci tree, no authoritative ACL store.
rpcd on RDK — Case Study
5

## Slide 6
04 — STRATEGY
One option ruled out immediately
Full replacement of RBUS / Thunder with ubus + rpcd
Not realistic. Not recommended. Would mean rewriting every CCSP component and every Thunder plugin's registration and RPC-handling code, discarding RDK's own TR-181 tooling (dmcli, ACS/TR-069 integration, RFC), and taking on an enormous, ongoing merge burden against every future RDK release. Not a serious option for an existing RDK deployment.
What's realistic instead: treat rpcd/ubus as an optional, isolated compatibility facade — bridged into RDK's real buses, not a wholesale platform swap. Two concrete strategies for that follow.
rpcd on RDK — Case Study
6

## Slide 7
04 — STRATEGY
Two realistic integration strategies
STRATEGY A
Isolated rpcd/ubus instance, bridged in
Run a genuine ubusd + rpcd, but write new native rpcd plugins whose init() opens an rbus_open() connection (RDK-B) or a Thunder COM-RPC/JSON-RPC client (RDK-V) internally — translating ubus calls into the real bus's calls and back. Same shape as rpcd's own built-in uci object, just bridging to RBUS/Thunder instead of libuci. uhttpd + uhttpd_ubus.so sits in front exactly as already built.
STRATEGY B
Extend RDK's own bridge instead
Skip ubus/rpcd on-device entirely. Thunder already has a JSON-RPC/WebSocket bridge with its own token auth, and RBUS already has get/set/subscribe semantics — teach whatever client tooling currently speaks ubus JSON-RPC to also speak Thunder's dialect or an RBUS-facing HTTP shim. Avoids a second bus and daemon on-device, at the cost of pushing translation work into the client/tooling side.
rpcd on RDK — Case Study
7

## Slide 8
Choosing between A and B
The choice depends entirely on which constraint is actually binding.
“The device must expose this exact
ubus/rpcd wire protocol”
→ favors Strategy A (on-device bridge plugin)
“The tooling must work against both
platforms, however it gets there”
→ favors Strategy B — usually cheaper, lower-risk
RDK-B is the stronger case for doing this at all — it has no existing browser-facing JSON-RPC/token-auth story the way RDK-V's Thunder does natively.
rpcd on RDK — Case Study
8

## Slide 9
05 — RDK-B DETAIL
RDK-B (Broadband) specific considerations
Translation is genuinely different shapes
RBUS is a hierarchical typed parameter tree (Device.WiFi.Radio.1.Channel) with get/set/method/event-subscribe — not ubus's flat object/method/argument-blob shape. A bridge plugin must map each rpcd object to RBUS parameters/methods/events and convert RBUS's typed values to/from blob_attr.
The built-in uci object is close to meaningless
RDK-B's real config is PSM + SysCfg + TR-181, not uci files. Either disable rpcd's built-in uci object on RDK-B builds, or replace it with a custom PSM-speaking bridge plugin — leaving it registered but backed by nothing would be actively misleading.
A real ubus/netifd may already exist, narrowly
Some RDK-B reference platforms carry OpenWrt-derived network components (a real ubus/netifd instance) under a CCSP wrapper on certain SoC BSPs. Worth checking per target platform — rpcd could attach there directly for network state, while everything else still needs the RBUS bridge.
ACL duplication and WAN exposure risk
RDK-B is typically WAN-managed via TR-069/TR-369, with RBUS's own ACL gating cross-component access. A second, independent rpcd ACL creates two sources of truth. Hard requirement: loopback/LAN-only, never WAN-facing, and re-check RBUS's own permissions rather than trusting rpcd's own grants.
rpcd on RDK — Case Study
9

## Slide 10
06 — RDK-V DETAIL
RDK-V (Video) specific considerations
The value proposition is honestly weaker
Thunder already provides a plugin-based, HTTP/JSON-RPC-over-WebSocket, token-authenticated RPC surface — the same category uhttpd + rpcd provides for OpenWrt. rpcd/ubus here mostly duplicates a solved problem; the strongest case is tooling uniformity, not filling a gap.
IARM-Bus bridging is narrower in scope
A native rpcd plugin here links against libIARM directly and translates specific events (power state, HDMI hotplug) into ubus methods/events — narrower than a full RBUS bridge, since IARM isn't a general data-model bus.
No ABI-level bridge between the two plugin models
rpcd native plugins are C, exporting one struct rpc_plugin symbol; Thunder plugins are C++ against Thunder's own base classes and COM-RPC vtables. Any bridge must be a standalone process speaking both protocols — not a plugin either side's loader can satisfy directly.
Two independent auth/session systems, again
Thunder's token-based Security Agent and rpcd's session.login/ACL model coexist, not merge. A bridge must require and validate a real Thunder token before trusting a ubus session — or accept it's a second, separately-secured path into plugins Thunder already gates.
rpcd on RDK — Case Study
10

## Slide 11
07 — CROSS-CUTTING
Engineering considerations — both profiles
Build system
RDK builds on Yocto/bitbake, not OpenWrt buildroot — every package (libubox, ubus, uci, rpcd) needs new .bb recipes. Straightforward (all four are portable C, proven to build clean on plain glibc) but real, uncounted work.
Footprint
RDK-B/V devices already run many long-lived daemons. Adding ubusd, rpcd, and bridge process(es) is additional RAM/CPU/flash on tightly budgeted hardware — needs a real sizing pass, not just “it built and ran.”
Security review
Both profiles typically require operator-mandated security certification for any new IPC surface. Key question: does the bridge faithfully re-derive and re-check the caller's real permissions on every call, or become a trusted, always-privileged path that silently bypasses RBUS/Thunder's own ACL?
Ongoing maintenance
libubox/ubus/uci/rpcd are maintained upstream, independent of RDK. A vendored copy needs an explicit plan for tracking upstream security fixes and re-validating against each new RDK release — a standing commitment, not a one-time port.
Verification redone per bus
Every claim this project verified about ubus/rpcd (nm -D, strace, live ACL tests, HTTP captures) was verified for ubus specifically. None of it transfers automatically to RBUS's or Thunder's actual runtime behavior.
rpcd on RDK — Case Study
11

## Slide 12
08 — GO / NO-GO
Decision checklist
Is the actual goal tooling uniformity, not replacing RDK's IPC?
If “no” → stop / redesign
Can the bridge be strictly loopback / LAN-scoped, never WAN-reachable?
If “no” → stop / redesign
Can the bridge re-derive and re-check permissions against RBUS's / Thunder's own ACL on every call, rather than trusting its own grant?
If “no” → stop / redesign
Does the target platform's footprint budget have headroom for ubusd + rpcd + a bridge process?
If “no” → stop / redesign
Is there a concrete plan for tracking upstream ubus/rpcd security fixes going forward?
If “no” → stop / redesign
rpcd on RDK — Case Study
12

## Slide 13
Summary
rpcd cannot be “enabled” on RDK by flipping a build flag.
It has no bus to register objects on, no config tree to read, and no ACL/session model authoritative over anything RDK actually enforces — on either profile.
RDK-B
Stronger case for doing this — no native browser-facing JSON-RPC/token-auth story exists today.
RDK-V
Weaker case — Thunder already solves this natively; only tooling-uniformity justifies duplicating it.
The hard engineering risk isn't compiling rpcd for a new target — that's the easy part, already proven in this project. It's correctly reconciling two independent authorization systems without opening a privilege-escalation path between them.
rpcd on RDK — Case Study
13